## Slide 1
BHARTI INFOTECH AND SERVICES
Bilaspur , Chhattisgarh
Introduction to Sensors

## Slide 2: Introduction
To be useful, systems must interact with their environment. To do this they use sensors and actuators
Sensors and actuators are examples of transducers
A transducer is a device that converts one physical quantity into another
  - examples include:
    a mercury-in-glass thermometer (converts temperature into displacement of a column of mercury)
    a microphone (converts sound into an electrical signal).
We will look at sensors in this lecture and at actuators in the next lecture.

## Slide 3
  - widely used sensors include those that are:
    resistive
    inductive
    capacitive
    piezoelectric
    photoresistive
    elastic
    thermal.
Almost any physical property of a material that changes in response to some excitation can be used to produce a sensor

## Slide 4: Describing Sensor Performance
Range
  maximum and minimum values that can be measured
Resolution or discrimination
  smallest discernible change in the measured value
Error
  difference between the measured and actual values
    random errors
    systematic errors
Accuracy, inaccuracy, uncertainty
  accuracy is a measure of the maximum expected error

## Slide 5
Precision
  - a measure of the lack of random errors (scatter)

## Slide 6
Linearity
  - maximum deviation from a ‘straight-line’ response
  - normally expressed as a percentage of the full-scale value
Sensitivity
  - a measure of the change produced at the output for a given change in the quantity being measured

## Slide 7
Temperature sensors
Resistive thermometer
- typical devices use platinum wire (such a device is called a platinum resistance thermometers or PRT)
  - linear but has poor sensitivity
A typical PRT element
  A sheathed PRT

## Slide 8
Thermistors
  use materials with a high thermal coefficient of resistance
  Sensitive but highly non-linear
  A typical disc thermistor A threaded thermistor

## Slide 9
pn junctions
  a semiconductor device with the properties of a diode (we will consider semiconductors and diodes later)
  inexpensive, linear and easy to use
  limited temperature range (perhaps -50C to 150 C) due to nature of semiconductor material
pn-junction sensor

## Slide 10: Light Sensors
Photovoltaic
  light falling on a pn-junction can be used to generate electricity from light energy (as in a solar cell)
  small devices used as sensors are called photodiodes
  fast acting, but the voltage produced is not linearly related to light intensity
A typical photodiode

## Slide 11
Photoconductive
  such devices do not produce electricity, but simply change their resistance
  photodiode (as described earlier) can be used in this way to produce a linear device
  phototransistors act like photodiodes but with greater sensitivity
  light-dependent resistors (LDRs) are slow, but respond like the human eye
A light-dependent resistor (LDR)

## Slide 12: Force Sensors
Strain gauge
  stretching in one direction increases the resistance of the device, while stretching in the other direction has little effect
  can be bonded to a surface to measure strain
  used within load cells and pressure sensors
A strain gauge
Direction of sensitivity

## Slide 13: Displacement Sensors
Potentiometers
  resistive potentiometers are one of the most widely used forms of position sensor
  can be angular or linear
  consists of a length of resistive material with a sliding contact onto the resistive track
  when used as a position transducer a potential is placed across the two end terminals, the voltage on the sliding contact is then proportional to its position
  an inexpensive and easy to use sensor

## Slide 14: Motion Sensors
Motion sensors measure quantities such as velocity and acceleration
  can be obtained by differentiating displacement
  differentiation tends to amplify high-frequency noise
Alternatively can be measured directly
  some sensors give velocity directly
    e.g. measuring frequency of pulses in the counting techniques described earlier gives speed rather than position
  some sensors give acceleration directly
    e.g. accelerometers usually measure the force on a mass

## Slide 15: Sound Sensors
Microphones
  a number of forms are available
    e.g. carbon (resistive), capacitive, piezoelectric and moving-coil microphones
    moving-coil devices use a magnet and a coil attached to a diaphragm – we will discuss electromagnetism later

## Slide 16: Sensor Interfacing
Resistive devices
  can be very simple
    e.g. in a potentiometer, with a fixed voltage across the outer terminals, the voltage on the third is directly related to position
    where the resistance of the device changes with the quantity being measured, this change can be converted into a voltage signal using a potential divider – as shown
    the output of this arrangement is not linearly related to the change in resistance

## Slide 17
Switches
  - switch interfacing is also simple
    can use a single resistor as below to produce a voltage output
    all mechanical switches suffer from switch bounce

## Slide 18
Capacitive and inductive sensors
  sensors that change their capacitance or inductance in response to external influences normally require the use of alternating current (AC) circuitry
  such circuits need not be complicated
  we will consider AC circuits in later lectures